## Slide 1: Electroencephalography (EEG)
Jan Kudláček
2022-04-08
kudlaceksystem@gmail.com

## Slide 2: Electroencephalography (EEG)
Hans Berger (1873-1941)
Alpha activity
1 s
100 μV
Electrical activity of the brain

## Slide 3: Electroencephalography(EEG)
Recording of electrical potentials caused by the brain activity
  Electroencephalograph – instrument
  Electroencephalogram – recording
Scalp (surface) EEG records the activity of the cortical neurons in the vicinity of the electrode
Method of functional examination
Diagnosis of brain disorders
  Epilepsy
  Sleep disorders
Weak signal
  In the order of 100 µV
  E.g. ECG is around 1 mV

## Slide 4
Presynaptický
neuron
Postsynaptický
neuron
Neurophysiology of synaptic transmission

## Slide 5
Presynaptic
neuron
Postsynaptic
neuron
Neurophysiology of synaptic transmission

## Slide 6
Action potential
Neurophysiology of synaptic transmission
Presynaptic
neuron
Postsynaptic
neuron

## Slide 7
Excitatory postsynaptic potential (EPSP)
Neurophysiology of synaptic transmission
Presynaptic
neuron
Postsynaptic
neuron
Action potential

## Slide 8
EPSP2
EPSP1
Sum
Presynaptic
neuron I
Postsynaptic
neuron
Presynaptic
neuron II
Spatial summation of postsynaptic potentials

## Slide 9
Temporal summation of postsynaptic potentials
Presynaptic
neuron
Postsynaptic
neuron
Presynaptický
neuron
EPSP1
EPSP2
Sumace

## Slide 10
Cellular mechanisms of the EEG
Pyramidal
neuron
Apical dendritic tree
Soma
Main source of EEG
  Synaptic activity on pyramidal neurons
Pyramidal neurons
  Main projection neurons in the cortex
  Apical dendrites perpendicular to the brain surface
Extracellular currents and electric fields
  Synaptic activity
  No contribution of action potentials
Two pyramidal neurons

## Slide 11: Patch clamp
Brain slices
Cell cultures
Recording from a single cell
Whole-cell patch clamp

## Slide 12: Spontaneous postsynaptic currents

## Slide 13: Depolarizing pulses, action potentials
Pyramidal neuron
Parvalbumine-positive inhibitory interneuron

## Slide 14: Origin of EEG signal

## Slide 15: Origin of EEG signal

## Slide 16: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 17: Origin of EEG signal
Extracellular recording
Intracellular recording
Scalp EEG
Extracellular recording

## Slide 18: Origin of EEG signal
Extracellular recording
Intracellular recording
Scalp EEG
Extracellular recording

## Slide 19: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 20: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 21: Origin of EEG signal
Extracellular recording
Intracellular recording
Scalp EEG
Extracellular recording

## Slide 22: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 23: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 24: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 25: Origin of EEG signal
Extracellular recording
Intracellular recording
Scalp EEG
Extracellular recording

## Slide 26: Lines of force and equipotential lines
-100 uV
-200 uV
-300 uV
-400 uV
-500 uV
100 uV
200 uV
300 uV
400 uV
500 uV
0 uV
0 uV
-100 uV
voltage
100 uV
200 uV
-200 uV
current

## Slide 27: Morphology, amplitude a duration of EEG waves
Distance from the current generator
Duration of the postsynaptic potentials
Number of synchronous postsynaptic potentials
Position of the electrode with respect to the current generator
Anatomical orientation of the cells generating the currents

## Slide 28: Morphology, amplitude a duration of EEG waves
Distance from the current generator
Duration of the postsynaptic potentials
Number of synchronous postsynaptic potentials
Position of the electrode with respect to the current generator
Anatomical orientation of the cells generating the currents

## Slide 29
-100 uV
-200 uV
-300 uV
-400 uV
-500 uV
100 uV
200 uV
300 uV
400 uV
500 uV
0 uV
0 uV
-100 uV
-200 uV
100 uV
200 uV
-100 uV

## Slide 30
-100 uV
-200 uV
-300 uV
-400 uV
-500 uV
100 uV
200 uV
300 uV
400 uV
500 uV
0 uV
0 uV
-100 uV
-200 uV
100 uV
200 uV
-500 uV
-100 uV

## Slide 31
-100 uV
-200 uV
-300 uV
-400 uV
-500 uV
100 uV
200 uV
300 uV
400 uV
500 uV
0 uV
0 uV
-100 uV
-200 uV
100 uV
200 uV
-500 uV
-100 uV
??? uV

## Slide 32: Morphology, amplitude a duration of EEG waves
Distance from the current generator
Duration of the postsynaptic potentials
Number of synchronous postsynaptic potentials
Position of the electrode with respect to the current generator
Anatomical orientation of the cells generating the currents

## Slide 33
0.4 s
100 uV
EEG
Normal brain activity

## Slide 34
0.4 s
100 uV
EEG
Epileptic discharges

## Slide 35: Morphology, amplitude a duration of EEG waves
Distance from the current generator
Duration of the postsynaptic potentials
Number of synchronous postsynaptic potentials
Position of the electrode with respect to the current generator
Anatomical orientation of the cells generating the currents

## Slide 36
EEG
–
activity from the top of the gyrus

## Slide 37
EEG
–
activity from the depth of the gyrus not seen in EEG
(could be seen in MEG)

## Slide 38: Morphology, amplitude a duration of EEG waves
Distance from the current generator
Duration of the postsynaptic potentials
Number of synchronous postsynaptic potentials
Position of the electrode with respect to the current generator
Anatomical orientation of the cells generating the currents

## Slide 39
EEG
aferent fibers

## Slide 40
EEG
aferent fibers

## Slide 41
EEG
aferent fibers

## Slide 42
Scalp EEG
Intracranial EEG
Local field potentials (LFP)
Extracellularly recorded action potentials
> 1 cm
< 1 cm
~ 1 mm
~ 10 um
Electrodes
Notes: Nase práce vychází z klinických pozorování

## Slide 43: Scalp EEG
Notes: Nase práce vychází z klinických pozorování

## Slide 44
Fp1
Fz
F3
F7
T3
C3
Cz
Pz
P3
T5
Fp2
F4
C4
Scalp EEG – electrode positions
International 10-20 system

## Slide 45
International 10-20 system
Scalp EEG – electrode positions

## Slide 46: Montage
Positions of electrodes and type of referencing of the signals
Referential montage
  Scalp (active) electrode with respect to a reference (neutral) electorde
Bipolar (sequential) montage
  Scalp (active) electrode with respect to another scalp electorde

## Slide 47
EEG – referential montage
+
-
1
0
0
0
0
0
0
0
0
0
Reference electrode
1
0
0
0
0
Active electrode
EEG trace
Differential amplifier

## Slide 48
+
-
0
0
0
0
0
-1
0
0
0
0
-1
0
0
0
0
Reference electrode
Active electrode
EEG trace
Differential amplifier
EEG – referential montage

## Slide 49
EEG – referential montage

## Slide 50
+
-
1
0
0
0
0
0.75
0
0
0
0
Active electrode 1
EEG trace
Differential amplifier
0.25
0
0
0
0
EEG – bipolar montage
Active electrode 2

## Slide 51
+
-
1
0
0
0
0
0
0
0
0
0
1
0
0
0
0
Active electrode 1
EEG trace
Differential amplifier
EEG – bipolar montage
Active electrode 2

## Slide 52
+
-
1 mV
0
0
0
0
-1 mV
0
0
0
0
2 mV
0
0
0
0
Active electrode 1
EEG trace
Differential amplifier
EEG – bipolar montage
Active electrode 2

## Slide 53
EEG – longitudinal bipolar montage

## Slide 54
EEG – transversal bipolar montage

## Slide 55: Deep structures
Deep structures
  Hippocampus
  Thalamus
  Brain stem
No contribution to scalp EEG
Indirect effect on the EEG

## Slide 56
Supplementary anterior temporal electrodes
Fp1
Fz
F3
F7
T3
C3
Cz
Pz
P3
T5
Fp2
F4
C4

## Slide 57
Sphenoidal electrodes

## Slide 58
Intracranial (invasive) EEG

## Slide 59
EEG frequency bands
0,5-4 Hz
4-8 Hz
13-30 Hz
α
δ
ϑ
β
8-13 Hz
1 s
100 uV

## Slide 60
Event duration
Period/frequency
Wave duration
Amplitude
Spike-wave complex
Wave
Spike
Spike duration
300 ms
100 uV
Notes: Nase práce vychází z klinických pozorování

## Slide 61: Waking EEG

## Slide 62: Temporal lobe epilepsy

## Slide 63: Temporal lobe epilepsy

## Slide 64
Fp1
Fz
F3
F7
T3
C3
Cz
Pz
P3
T5
Fp2
F4
C4
Supplementary anterior temporal electrodes

## Slide 65: Temporal lobe epilepsy with the supplementary anterior temporal electrodes

## Slide 66: Absence seizure
Notes: Nase práce vychází z klinických pozorování

## Slide 67: Evoked potentials – recording

## Slide 68
+
Evoked response
Background activity
10x averaging
100x averaging
200x averaging
500x averaging
1000x averaging
3000x averaging
Evoked potentials – averaging

## Slide 69: Brainstem Auditory Evoked Potentials
I - auditory nerve
II - cochlear
III - superior olivary nuclei
IV - lateral lemniscus
V - inferior colliculi
II+III - pons
IV+V - midbrain
Left ear stimulation at 60 dB.

## Slide 70: Visual evoked potentials
Pattern reversal evoked potentials
Or just blinking (infants, comatose patients)
Diagnosis of multiple sclerosis, demyelination related diseases, etc.

## Slide 71: Visual evoked potentials
Healthy eye
Diseased eye

## Slide 72: Sleep

## Slide 73: What is the sleep?
Basic physiological need
Behavioral state
  Reversible
  Low interaction with environment
  Decrease motor activity
  Stereotype postures

## Slide 74: Polysomnography
Monitoring of various physiological signals during sleep

## Slide 75: Sleep stages
REM (Rapid eye movements)
  Rapid eye movements
  Muscle atonia
    Not in REM behavioral disorder (RBD)
  Increased neuronal activity
  Increased metabolism
  EEG similar to waking
  “Paradoxical sleep”
  Vivid dreams
Non-REM
  Classification NREM 1-3
  Alternatively Stage 1-4
  Low neuronal activity
  The lowest level of the brain metabolism
  Decrease of sympathetic activity
  Muscle tone and reflexes intact

## Slide 76: Sleep EEG
B
A
T
S
Drink
Blood
4-7 Hz
12-30 Hz
8-12 Hz
1-4 Hz
1-4 Hz
12-30 Hz

## Slide 77: Hypnogram, sleep cycles
Cycle duration 90 – 110 minutes
4 – 6 cycles per night

## Slide 78: Physiological changes during sleep

## Slide 79: Physiological changes during sleep
Heart rate
Respiration
Penile erection

## Slide 80: Sleep during development and aging

## Slide 81: Wakefulness and sleep-wake transitions
Ascending reticular activating system (ARAS)
  All components innervated by orexin neurons
  Connections to cortex, etc.
Orexin/hypocretin
  Neuropeptide
  Maintains wakefulness
  Only 10 000 to 20 000 orexin neurons in human brain
  Lack of orexin neurons -> narcolepsy

## Slide 82: Narcolepsy
Sleep disorder
Excessive daytime sleepiness
Sleep attacks with sudden atonia
Initiation with REM sleep
Cataplexy
  Sudden atonia while conscious
  Descendent inhibitory system
Lessened quality of sleep

## Slide 83: Narcolepsy
Mechanism
  Loss of orexin neurons
Causes
  Genetic predisposition
  Environmental factors
    Autoimmune disorder triggered by H1N1 infection
Treatment
  Amphetamines
  Tricyclic antidepressants
  Orexin
normal hypothalamus
narcolepsy

## Slide 84: Role of sleep
Not entirely elucidated
Important for cognition
  Memory consolidation
Toxin clearing
Immune system more active during sleep
Sleep deprivation
  Followed by sleep compensation
  If severe, can lead to death

## Slide 85: Circadian rhythms

## Slide 86: Circadian rhythm
Changes in behavior due to alternating day and night
Predicting the day and night advantageous
Circadian clock developed in all organisms

## Slide 87: Molecular mechanism
Molecular oscillator in each cell on earth
Principle: The protein product inhibits its own transcription by feedback mechanism
In the human body, the cells need to be synchronized
  Suprachiasmatic nucleus (SCN)

## Slide 88: Synchronization by SCN
Ganglion cells in the retina (not rods or cones)
Send information about daylight to the suprachiasmatic nucleus (SCN)

## Slide 89: Damage to SCN
Normal
SCN lesion

## Slide 90: Free-running period
In constant darkness (or constant light)
The SCN oscillates at approx. 24 hour period
In most humans, around 25 hours

## Slide 91: Chronotherapy
Administration of drugs (or other treatment) at the time when it is most effective/has least adverse effects
  Heart attacks most probable in the morning due to highest blood pressure -> the best time for taking the drugs for blood pressure
  Antiseizure medication administered at the time when most seizure occur
  etc.

## Slide 92: Thank you for your attention
Questions?
Comments?
Suggestions?
kudlaceksystem@gmail.com